## Slide 1: Intensity Transformation and Spatial Filtering

## Slide 3: Spatial Domain Process

## Slide 4: Spatial Domain Process

## Slide 5: Spatial Domain Process

## Slide 6: Arithmetic operations and clipping

## Slide 8: Some Basic Intensity Transformation Functions

## Slide 9: Image Negatives

## Slide 10: Example: Image Negatives

## Slide 11: Log Transformations

## Slide 12: Example: Log Transformations

## Slide 13: Power-Law (Gamma) Transformations

## Slide 14: Example: Gamma Transformations

## Slide 15: Example: Gamma Transformations
Cathode ray tube (CRT) devices have an intensity-to-voltage response that is a power function, with exponents varying from approximately 1.8 to 2.5

## Slide 16: Example: Gamma Transformations

## Slide 17: Example: Gamma Transformations

## Slide 18: Piecewise-Linear Transformations
Contrast Stretching
— Expands the range of intensity levels in an image so that it spans the full intensity range of the recording medium or display device.
Intensity-level Slicing
— Highlighting a specific range of intensities in an image often is of interest.
output = output_start + ((output_end - output_start) / (input_end - input_start)) * (input - input_start)

## Slide 20
Highlight the major blood vessels and study the shape of the flow of the contrast medium (to detect blockages, etc.)
Measuring the actual flow of the contrast medium as a function of time in a series of images

## Slide 21: Bit-plane Slicing

## Slide 22: Bit-plane Slicing

## Slide 23: Bit-plane Slicing

## Slide 24: Merging two images
M = top (mask) image, I = lower image
E = M + I
Multiply, E = M x I/ 255
Screen, E = 255 – ((255 - M) x (255 - I)) / 255
Overlay, E = (I / 255) x (I + (2xM/255) x (255 - I))
Dodge, E = 256 x I / ((255 - M) + 1)
Burn, E = 255 – (256 x (255- I) / (M + 1))
For more https://docs.gimp.org/en/gimp-concepts-layer-modes.html
https://en.wikipedia.org/wiki/Blend_modes
https://es.mathworks.com/matlabcentral/fileexchange/43122-blend-images

## Slide 25: Assignment#1 Discussion
Posterize: Usually values within [0,255] represent a pixel. Instead of using 256 colors, you have to use less number of colors like 4-8. Every pixel will get the closest output color.
Nightvision: Output R = Input G / 2, Output B = 2 x Output R, Output G = 2 x Output B
Photocopy: Convert the input to gray level image. Then, consider a threshold = 100. If a pixel value is greater than the threshold, put 255 as the color value in the output. Otherwise, put input pixel x (threshold - input pixel) / (threshold^2) as the output pixel.
Vignetting: Calculate the center pixel of the image and the maximum distance (M) possible from the center to any corner. Then, go to each pixel and calculate the distance (D) from that pixel location to the center. Find a darkness weight = 1 - D / M. For the output pixel, multiply the weights with the input pixel value.
Mirror Image: We can get the mirror image of the given image if we reverse the order of the pixels (elements of the matrix) in each row.

## Slide 27: Histogram Equalization

## Slide 29: Histogram Equalization

## Slide 30: Example: Histogram Equalization
Suppose that a 3-bit image (L=8) of size 64 × 64 pixels (MN = 4096) has the intensity distribution shown in following table.
Get the histogram equalization transformation function and give the ps(sk) for each sk.

## Slide 31: Example: Histogram Equalization

## Slide 32: Example: Histogram Equalization

## Slide 34: Histogram Matching: Discrete Cases
Obtain pr(rj) from the input image and then obtain the values of sk, round the value to the integer range [0, L-1].
Use the specified PDF and obtain the transformation function G(zq), round the value to the integer range [0, L-1].
Mapping from sk to zq

## Slide 35: Example: Histogram Matching
Suppose that a 3-bit image (L=8) of size 64 × 64 pixels (MN = 4096) has the intensity distribution shown in the following table (on the left). Get the histogram transformation function and make the output image with the specified histogram, listed in the table on the right.

## Slide 36: Example: Histogram Matching
Obtain the scaled histogram-equalized values,
Compute all the values of the transformation function G,

## Slide 37: Example: Histogram Matching

## Slide 38: Example: Histogram Matching
Obtain the scaled histogram-equalized values,
Compute all the values of the transformation function G,
s0
s2
s3
s5
s6
s7
s1
s4

## Slide 39: Example: Histogram Matching

## Slide 40: Example: Histogram Matching
Further readining:
https://automaticaddison.com/difference-between-histogram-equalization-and-histogram-matching/

## Slide 41: Example: Histogram Matching

## Slide 42: Example: Histogram Matching

## Slide 43: Example: Histogram Matching

## Slide 44: Local Histogram Processing
Define a neighborhood and move its center from pixel to pixel
At each location, the histogram of the points in the neighborhood is computed. Either histogram equalization or histogram specification transformation function is obtained
Map the intensity of the pixel centered in the neighborhood
Move to the next location and repeat the procedure

## Slide 45: Local Histogram Processing: Example

## Slide 46: Spatial Filtering
A spatial filter consists of (a) a neighborhood, and (b) a predefined operation
Linear spatial filtering of an image of size MxN with a filter of size mxn is given by the expression

## Slide 47: Spatial Filtering

## Slide 49: Spatial Correlation

## Slide 50: Spatial Convolution

## Slide 52: Smoothing Spatial Filters
Smoothing filters are used for blurring and for noise reduction
Blurring is used in removal of small details and bridging of small gaps in lines or curves
Smoothing spatial filters include linear filters and nonlinear filters.

## Slide 53: Spatial Smoothing Linear Filters

## Slide 54: Two Smoothing Averaging Filter Masks

## Slide 56: Example: Gross Representation of Objects

## Slide 57: Order-statistic (Nonlinear) Filters
— Nonlinear
— Based on ordering (ranking) the pixels contained in the filter mask
— Replacing the value of the center pixel with the value determined by the ranking result
E.g., median filter, max filter, min filter

## Slide 58: Example: Use of Median Filtering for Noise Reduction

## Slide 59: Sharpening Spatial Filters
Foundation
Laplacian Operator
Unsharp Masking and Highboost Filtering
Using First-Order Derivatives for Nonlinear Image Sharpening — The Gradient

## Slide 60: Sharpening Spatial Filters: Foundation
The first-order derivative of a one-dimensional function f(x) is the difference
The second-order derivative of f(x) as the difference

## Slide 63: Sharpening Spatial Filters: Laplace Operator
The second-order isotropic derivative operator is the Laplacian for a function (image) f(x,y)

## Slide 64: Sharpening Spatial Filters: Laplace Operator

## Slide 65: Sharpening Spatial Filters: Laplace Operator
Image sharpening in the way of using the Laplacian:

## Slide 67: Unsharp Masking and Highboost Filtering
Unsharp masking
Sharpen images consists of subtracting an unsharp (smoothed) version of an image from the original image
e.g., printing and publishing industry
Steps
1. Blur the original image
2. Subtract the blurred image from the original
3. Add the mask to the original

## Slide 68: Unsharp Masking and Highboost Filtering

## Slide 69: Unsharp Masking: Demo

## Slide 70: Unsharp Masking and Highboost Filtering: Example

## Slide 71: Image Sharpening based on First-Order Derivatives
Gradient Image

## Slide 72: Image Sharpening based on First-Order Derivatives
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9

## Slide 73: Image Sharpening based on First-Order Derivatives
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9

## Slide 74: Image Sharpening based on First-Order Derivatives

## Slide 75: Example

## Slide 76: Example: Combining Spatial Enhancement Methods Goal: Enhance the image by sharpening it and by bringing out more of the skeletal detail

## Slide 77
Example: Combining Spatial Enhancement Methods Goal: Enhance the image by sharpening it and by bringing out more of the skeletal detail

## Slide 78
Blurring masks
A blurring mask has the following properties.
All the values in blurring masks are positive
The sum of all the values is equal to 1
The edge content is reduced by using a blurring mask
As the size of the mask grow, more smoothing effect will take place
Derivative masks
A derivative mask has the following properties.
A derivative mask have positive and as well as negative values
The sum of all the values in a derivative mask is equal to zero
The edge content is increased by a derivative mask
As the size of the mask grows , more edge content is increased
Blurring masks are also called as low pass filter
Derivative masks are also called as high pass filter

## Slide 79: Gaussian Smoothing/Blur
The Gaussian distribution in 1-D has the form:
In 2-D, an isotropic (i.e. circularly symmetric) Gaussian has the form:

## Slide 80: Set and Logical Operations

## Slide 81: Set and Logical Operations
Let A be the elements of a gray-scale image
The elements of A are triplets of the form (x, y, z), where x and y are spatial coordinates and z denotes the intensity at the point (x, y).
The complement of A is denoted Ac

## Slide 82: Set and Logical Operations
The union of two gray-scale images (sets) A and B is defined as the set

## Slide 83: Set and Logical Operations

## Slide 84: Set and Logical Operations

## Slide 85: Geometric Spatial Transformations
Geometric transformation (rubber-sheet transformation)
— A spatial transformation of coordinates
— intensity interpolation that assigns intensity values to the spatially transformed pixels.
Affine transform

## Slide 87: Intensity Assignment
Forward Mapping: scanning the pixels of the input image and, at each location ( x, y) computing the spatial location (x’ , y’)of the corresponding pixel in the output image
It’s possible that two or more pixels can be transformed to the same location in the output image.
Inverse Mapping
The nearest input pixels to determine the intensity of the output pixel value.
Inverse mappings are more efficient to implement than forward mappings.

## Slide 88: Example: Image Rotation and Intensity Interpolation

## Slide 89: Image Registration
Input and output images are available but the transformation function is unknown.
Goal: estimate the transformation function and use it to register the two images.
One of the principal approaches for image registration is to use tie points (also called control points)
The corresponding points are known precisely in the input and output (reference) images.

## Slide 91: Image Registration
A simple model based on bilinear approximation:

## Slide 92: Image Registration

## Slide 93: Color space: RGB
A color space is a specific organization of colors.
In combination with color profiling supported by various physical devices, it supports reproducible representations of color -- whether such representation entails an analog or a digital representation.

## Slide 94: HSI Color space
The Hue, which can be defined rate of pure color, is an angle form between 0° and 360°. Red, Green, Blue are 0°, 120°, and 360°, and Yellow, Cyan, and Magenta are 60°, 180°, 300°.
The Saturation, which shows how the color to be pure, takes value between [0, 1].
The intensity is the dimensions of lightness or darkness. The range of intensity is between 0 (black) and 1 (white).

## Slide 95: YIQ Color space
YIQ, which is defined by the National Television System Committee (NTSC), produces the luminance and the chrominance.
The Y component represents the luma information, and is the only component used by black-and-white television receivers. I and Q represent the chrominance information.

## Slide 96: Noise
We may define noise to be any degradation in the image signal, caused by external disturbance.
If an image is being sent electronically from one place to another, via satellite or wireless transmission, or through networked cable, we may expect errors to occur in the image signal. These errors will appear on the image output in different ways depending on the type of disturbance in the signal.
Cleaning an image corrupted by noise is thus an important area of image restoration

## Slide 97: Salt and pepper noise
Also called impulse noise, shot noise, or binary noise.
This degradation can be caused by sharp, sudden disturbances in the image signal; its appearance is randomly scattered white or black (or both) pixels over the image.

## Slide 98: Gaussian noise
Gaussian noise is an idealized form of white noise, which is caused by random fluctuations in the signal.
We can observe white noise by watching a television which is slightly mistuned to a particular channel. Gaussian noise is white noise which is normally distributed.
If the image is represented as ‘I’ and the Gaussian noise, ‘N’ by then we can model a noisy image by simply adding the two:
noisy image = I + N

## Slide 99: Speckle noise
Whereas Gaussian noise can be modelled by random values added to an image; speckle noise (or more simply just speckle) can be modelled by random values multiplied by pixel values, hence it is also called multiplicative noise.
noisy image = I (1+ N)

## Slide 100: Periodic noise
If the image signal is subject to a periodic, rather than a random disturbance, we might obtain an image corrupted by periodic noise.
The effect is of bars over the image.

## Slide 101: Noise cleaning/removal
Average filtering
Median filtering
Rank-order filtering
  Rather than take the median of a set, we order the set and take the -th value, for some predetermined value of .
Outlier method
Image averaging